|  | FLINT HILL FIRE DEPARTMENT STANDARD OPERATING GUIDELINE |
| --- | --- |

Guideline Number: 501.02

Guideline Title: Hose Maintenance

Adopted:   01/17/2014

Rescinds:  New

Approved By:   							 (Chief)

- PURPOSE:

This guideline describes the fire hose maintenance standards and processes used by the Flint Hill Fire Department (FHFD).

- DISCUSSION:

Reliability of fire hose in emergency situations is essential to completion of the public safety mission of the FHFD.  Proper maintenance of fire hose is a key factor in keeping hose in a state of readiness. This guideline details how fire hose should be inspected, cleaned and dried.  Testing is also a key component of fire hose readiness and is addressed separately in SOG 501.1 HOSE TESTING.

- GUIDELINE:

Inspection

- Check for chemical damage, burns, cuts or abrasions to the outer jacket.

- Look for lumps or protrusions which may indicate twisting, separation or weak spots in the inner liner.

- Look for out of round couplings.

- For NST hose

  - Carefully inspect the threads for burrs or other damage.

  - Verify the female coupling swivels smoothly

  - Verify the female coupling has a viable gasket

- For Storz hose

  - Inspect the coupling lugs and mating surfaces for damage

  - Verify the gaskets are in good condition

Cleaning

- Fire hose should be cleaned whenever it becomes dirty.

- Most mud or debris can be removed with a water stream (garden hose) and brush.

  - Lay the hose out flat on a hard surface, 1 section at a time. The front pad of Station 1 is a good location to do this.

  - Multiple sections may be laid side by side so more than one can be sprayed and brushed with a broom at the same time.

  - Flip the hose over and spray/brush the opposite side.

  - If mud, dirt, debris, etc collects in the area where the hose is being cleaned stop cleaning hose and remove the dirt before continuing.

  - If stubborn stains or dirt remains on the hose use a truck wash soap solution in a mop bucket and stiff bristle brush to remove the substance. Rinse thoroughly.

- Lightly soiled hose can be washed using the hose washer

  - Connect the washer to Tanker 1 or an engine and set pressure to about50 psi.

  - Slowly pass the hose through the washer. The washer will pull the hose through quickly so some tension will have to be put on it.

  - Multiple passes may be necessary to sufficiently clean the hose.

  - Stuck on soil will require more complete cleaning as described in this guideline.

Drying

- Hose should be dried out of direct sunlight.

- Do not dry hose on blacktop.

- Do not dry hose outside.

- Preferred method is to flake the hose in an accordion fashion on its side on the bay floor.

  - Leave space between the flakes so air can circulate around the hose to shorten drying time.

  - At Station 1 this can be done between trucks and behind Ladder 1 toward the rear of the station.

  - At Station 2 this can be done between trucks.